## Slide 1
CS230-Wrapup

## Slide 2: From Performance to Security: 10K Feet View
2
Software
ISA
Registers
Caches, TLBs,
Branch predictors,
Prefetchers, Interconnect,
Out-of-order execution
ISA
Registers
Architecture

## Slide 3: Attacker
O3 processor ka, cache ka, prefetcher ka, coherence protocol ka, DRAM ka, sabka khabar lega 

## Slide 4: Security: A bit Subtle
Confidentiality
Integrity
Availability
You do not see (READ) what you are not supposed to see
You do not change (WRITE) what you are not supposed to see
You do not affect (DELAY) others (un)intentionally

## Slide 5: Attacks Inside

## Slide 6: Media Articles 

## Slide 7: Brushing-up: Information Leakage
Modular exponentiation, be mod n
Exponent e is used for decryption
Attacker tries to get the e
ei = 0, Square Reduce (SR)
ei = 1, SRMR
multiply
square
reduce

## Slide 8: Timing Channel
Adpated from flush+reload attack [Usenix Security ‘14]

## Slide 9: Toy Example: Flush Based Attacks
If secret=1 do
access(&a)
else // secret=0
no-access
Victim
flush(&a)
t1=start_timer
access(&a)
t2=end_timer
Attacker
Fast – 1
Slow – 0

## Slide 10: Side and Covert Channels
Side-channel attacks
Spy
Victim
Covert-channel attacks
Let’s play
Oh Yes!!

## Slide 11: Pause

## Slide 12: Flush+Reload Attack
LLC
12
Step 0:Spy maps the shared library, shared in the cache

## Slide 13: Flush+Reload Attack
Clflush
LLC
13
Step 0:Spy maps the shared library, shared in the cache
Step 1:Spy flushes the cache block

## Slide 14: Flush+Reload Attack
LLC
14
Step 0:Spy maps the shared library, shared in the cache
Step 1:Spy flushes the cache block
Step 2: Victim reloads the cache block

## Slide 15: Flush+Reload Attack
Step 0:Spy maps the shared library, shared in the cache
Step 1:Spy flushes the cache block
LLC
Step 2: Victim reloads the cache block
Step 3: Spy reloads the cache block (hit/miss)
Hit, Voila

## Slide 16: Pause

## Slide 17: How Practical?
Future is uncertain, if we do not take care of present attacks, future may be worse 

## Slide 18: Spectre and Meltdown

## Slide 19: Spectre in Action: Fasten Your Seat Belts
int CS230Array = [100, 200, 300];
int attacker = 4;
if (attacker < sizeof(CS230Array))
y = MyArray[CS230Array[attacker]*512]
DRAM LOAD
DRAM LOAD

## Slide 20: Branch Predictor and Speculative Execution
Branch predictor returns TRUE 
int CS230Array = [100, 200, 300];
int attacker = 4;
if (attacker < sizeof(CS230Array))
y = MyArray[CS230Array[attacker]*512]

## Slide 21: Branch Predictor and Speculative Execution
Branch predictor returns TRUE 
Attacker has mis-trained it  
T T T T T T T T T T T
How? By using values less than 3 always  
int CS230Array = [100, 200, 300];
int attacker = 4;
if (attacker < sizeof(CS230Array))
y = MyArray[CS230Array[attacker]*512]

## Slide 22: Branch Predictor and Speculative Execution
Branch predictor returns TRUE 
Attacker has mis-trained it  
Processor is on the wrong-path   
int CS230Array = [100, 200, 300];
int attacker = 4;
if (attacker < sizeof(CS230Array))
y = MyArray[CS230Array[attacker]*512]

## Slide 23: Branch Predictor and Speculative Execution
Branch predictor returns TRUE 
Attacker has mis-trained it  
Processor is on the wrong-path   
Branch resolution latency 200 cycles    
int CS230Array = [100, 200, 300];
int attacker = 4;
if (attacker < sizeof(CS230Array))
y = MyArray[CS230Array[attacker]*512]

## Slide 24: Within these 200 cycles 
CS230Array[4] is in L1/L2/L3 
The address is in the cache  
Yes, you guessed it right: F+R, P+P cache attacks   
int CS230Array = [100, 200, 300];
int attacker = 4;
if (attacker < sizeof(CS230Array))
y = MyArray[CS230Array[attacker]*512]

## Slide 25: Picture Abhi Baki Hai  After 200 cycles
y = MyArray[CS230Array[attacker]*512]
LOAD MyArray[0] 60 ns
LOAD MyArray[512] 60 ns
LOAD MyArray[1024] 5 ns Bingo !! CS230Array[attacker] = 2
Processor realized it was a mistake and
flushed all wrong path instructions
But cache has the data 

## Slide 26: Meltdown: The O3 Curse!!
raise_exception();
// line below is never reached
secret=KernelArray[data*4096];
secret=KernelArray[data*4096];
2. raise_exception();
Out-of-order (O3) as
it has no dependency
Kernel Trap
What about page-fault?

## Slide 27: Summary: CS230+CS231 (Connecting the dots on the board)