## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 11: Intro. to Single cycle CPU https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: Single Cycle Processor
All operations – single cycle 
Clock cycle (unit of time) will be defined based on the longest instruction.
Two paths of interest: datapath and control. Control tells datapath what to do.
Do not forget the stored program concept.

## Slide 4: Clock Cycle
Tick, clock tick, clock period, clock, clock cycle, or cycle
Discrete time intervals
Based on processor frequency (clock rate)
1GHz processor, clock cycle = 1ns
4GHz processor, clock cycle = 0.25ns

## Slide 5: Let’s start with the datapath
Anything that stores data or operates on data, within a processor

## Slide 6: Instruction Memory
32
Addr.
Instruction
32
Instr.
Mem
Remember: No writes to instruction memory 
Not concerned about how programs are loaded into this memory.

## Slide 7: Program Counter
32
32
PC
Remember: No writes to instruction memory 

## Slide 8: Register File
32
rd1
RegFile
32
rd2
Write Enable (a.k.a. register write)
32
wd
5
rs1
5
rs2
5
ws
rs1 and rs2: Read register 1 and 2
ws: Write register
wd: Write data

## Slide 9: The ALU
32
ALU
32
32
op

## Slide 10: Data Memory
32
Addr.
data
32
Data
Mem
data
32
Memory Read/Write
Why data and instruction memory and not one memory?
Later in the course 

## Slide 11: Address and Data Bus (Instruction Fetch)
32
Addr
Inst.
32
Instr
Mem
Fetching straight-line MIPS instructions requires a machine that generates this timing diagram:
CLK
Addr
Data
IMem[PC + 8]
IMem[PC + 4]
IMem[PC]
PC + 8
PC + 4
PC
PC == Program Counter, points to next instruction.

## Slide 12: Decode and Execute
32
rd1
RegFile
32
rd2
WE
32
wd
5
rs1
5
rs2
5
ws
32
ALU
32
32
op
opcode
rs
rt
rd
funct
shamt
Decode fields to get : ADD $8 $9 $10
Logic
Remember the opcode field
is the input to the control unit

## Slide 13: All in one go
32
Addr
Data
Instr
Mem
32
D
PC
Q
32
32
+
32
32
0x4
To rs1,
rs2, ws, op decode
logic ...
32
rd1
RegFile
32
rd2
WE
32
wd
5
rs1
5
rs2
5
ws
32
ALU
32
32
op

## Slide 14: What about I format?

## Slide 15: Loads from Memory
32
rd1
RegFile
32
rd2
WE
32
wd
5
rs1
5
rs2
5
ws
Ext
RegDest
ALUsrc
ExtOp
ALUctr
MemToReg
MemWr
Syntax: LW $1, 32($2)
Action: $1 = M[$2 + 32]
RegWr

## Slide 16: Branch Instructions
Clk
32
Instr Mem
Addr Data
32
D
PC
Q
32
32
+
32
32
0x4
Syntax: BEQ $1, $2, 12
Action: If ($1 != $2), PC = PC + 4 Action: If ($1 == $2), PC = PC + 4 + 48
PCSrc
32
+
32
Ex te nd

## Slide 17: Control Signals So far
MemRead
MemWrite
RegWrite
MemtoReg
RegDst
ALUop, ALUSrc
PCSrc (we have not discussed about the branch)
Read
address
Instruction
memory
Instruction
[31-0]
Control
I [31 - 26]
I [5 - 0]
RegWrite
ALUSrc
ALUOp
MemWrite
MemRead
MemToReg
RegDst
PCSrc
Zero

## Slide 18: In detail
MemRead: Read from memory when assert
MemWrite: Write into the memory when assert
RegWrite: Reg. on Write register updated with the input, on assert
MemtoReg: On assert, memory to register, on deassert, ALU to register
RegDst: On assert, use rd field, on deassert use rt field
ALUSrc: On assert, lower 16 bits of an inst., on deassert from the second register
PCSrc: On assert, branch target, deassert, PC+4

## Slide 19: Control Signal Table
Operation | RegDst | RegWrite | ALUSrc | ALUOp | MemWrite | MemRead | MemToReg
add | 1 | 1 | 0 | 010 | 0 | 0 | 0
sub | 1 | 1 | 0 | 110 | 0 | 0 | 0
and | 1 | 1 | 0 | 000 | 0 | 0 | 0
or | 1 | 1 | 0 | 001 | 0 | 0 | 0
slt | 1 | 1 | 0 | 111 | 0 | 0 | 0
lw | 0 | 1 | 1 | 010 | 0 | 1 | 1
sw | X | 0 | 1 | 010 | 1 | 0 | X
beq | X | 0 | 0 | 110 | 0 | 0 | X

## Slide 20: The Complete Picture
I[31-26]: Control unit

## Slide 21: Why not single cycle?
The longest possible datapath is the clock cycle time.
What does it mean?

## Slide 22: Why not single cycle?
one clock cycle: 8ns
Processor frequency: 125MHz
Cycle per Instruction (CPI): 1
An add instruction: no need of 8ns

## Slide 23: Why not single cycle?
The longest possible datapath is the clock cycle time.
Violating common case fast (Confucius says)

## Slide 24: Oh No! Such a bad design

## Slide 25: Single to Multi Cycle