## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 12: Instruction Pipelining
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: Single to Multi Cycle

## Slide 4: Single/multi-cycle (COVID19 vaccine schedule)
Single cycle (Worst case)
One shot will take 60 minutes one slot = 60 minutes
Multi cycle (average case kinda)
One shot: five to 60 minutes one slot = 15 minutes

## Slide 5: Can We Have Both?
Faster clock rate and also CPI=1?

## Slide 6: COVID19 Vaccination Schedule
Single cycle: one hour per person
verification: 25 minutes
5 minutes for vaccination
20 minutes post-vaccination
10 minutes, certificate 

## Slide 7: COVID19 Vaccination Schedule
Single cycle: Three hour, three persons
verification: 25 minutes
5 minutes for vaccination
20 minutes post-vaccination
10 minutes, certificate 

## Slide 8: COVID19 Vaccination Pipelined Schedule
Single cycle: one hour per person
Stage 1 verification: 15 minutes
Stage 2 verification: 10 minutes
Stage 3: 5 minutes for vaccination
Stage 4: 20 minutes post-vaccination
Stage 5: 10 minutes, certificate 

## Slide 9: COVID19 Vaccination Pipelined Schedule
Single cycle: one hour per person
Stage 1 verification: 15 minutes
Stage 2 verification: 10 minutes
Stage 3: 5 minutes for vaccination
Stage 4: 20 minutes post-vaccination
Stage 5: 10 minutes, certificate 

## Slide 10: COVID19 Vaccination Pipelined Schedule
Single cycle: one hour per person
Stage 1 verification: 15 minutes
Stage 2 verification: 10 minutes
Stage 3: 5 minutes for vaccination
Stage 4: 20 minutes post-vaccination
Stage 5: 10 minutes, certificate 

## Slide 11: COVID19 Vaccination Pipelined Schedule
Single cycle: one hour per person
Stage 1 verification: 15 minutes
Stage 2 verification: 10 minutes
Stage 3: 5 minutes for vaccination
Stage 4: 20 minutes post-vaccination
Stage 5: 10 minutes, certificate 

## Slide 12: COVID19 Vaccination Pipelined Schedule
Single cycle: one hour per person
Stage 1 verification: 15 minutes
Stage 2 verification: 10 minutes
Stage 3: 5 minutes for vaccination
Stage 4: 20 minutes post-vaccination
Stage 5: 10 minutes, certificate 

## Slide 13: COVID19 Vaccination Pipelined Schedule
Pipelined: One hour: Three persons
Stage 1 verification: 15 minutes
Stage 2 verification: 10 minutes
Stage 3: 5 minutes for vaccination
Stage 4: 20 minutes post-vaccination
Stage 5: 10 minutes, certificate 

## Slide 14: COVID19 Vaccination Pipelined Schedule
Pipelined: One hour: ? Persons, first person: 100 minutes , after a while throughput= 3 persons/hr
Stage 1 (20 mins): verification
Stage 2 (20 mins): verification
Stage 3 (20 mins): 5 minutes for vaccination
Stage 4 (20 mins): 20 minutes post-vaccination
Stage 5 (20 mins):10 minutes, certificate 
Think about variable stages, does it improve latency and throughput?

## Slide 15: Let’s pause a bit
Single cycle: CPI: 1 , Cycle time: long
Multi cycle: CPI: >1, Cycle time: short
Pipelined: CPI: 1, Cycle time: short (improves throughput but not latency)

## Slide 16: Latency and Bandwidth (throughput)
Latency
  time it takes to complete one instance
Throughput
  number of computations done per unit time

## Slide 17: Pipelining and Richard Feynman
https://www.youtube.com/watch?v=9miKIWIYi4w
Jump to 1:25

## Slide 18: Multi-cycle vs Pipelined
Multi-cycle
ins1.fetch ins1.(dec,ex) ins1.(mem,wb)
time
Pipelined
ins0.fetch ins0.(dec,ex) ins0.(mem,wb)
ins0.fetch ins0.(dec,ex) ins0.(mem,wb)
ins1.fetch ins1.(dec,ex) ins1.(mem,wb)
ins2.fetch ins2.(dec,ex) ins2.(mem,wb)

## Slide 19: Real World

## Slide 20: Vanilla 5-stage pipeline
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Memory
Reg File
MUX
MUX
Data
Memory
MUX
Sign
Extend
Zero?
IF/ID
ID/EX
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
Next SEQ PC
RD
RD
RD
WB Data
Next PC
Address
RS1
RS2
Imm
MUX
The right place to put the MUX that selects PC+4 and the target is the fetch stage.
The slide shows a vanilla 5-stage pipeline if we just take a single cycle datapath and divide it into five stages.

## Slide 21: Resource Utilization
Resources
t4
I5
I4
I3
I2
I1
we
addr
rdata
Data
wdata
Imm
Ext
addr
rdata
Inst.
IR
0x4
Add
we
PC
rs1
rs2
rd1
ws
wd rd2
GPRs
ALU
Memory
Memory
Write
I-Fetch
Decode, Reg. Fetch Execute
Memory
-
(IF)
(ID)
time t0 t1 t2 t3
(EX)
(MA)
t5 t6 t7 . . . .
Back
(WB)
IF
I1
I2
I3
I4
ID
I1
I2
I3
I5
EX
I1
I2
I4
I5
MA
I1
I3
I4
I5
WB
I2
I3
I4
I5

## Slide 22: Visualizing Pipeline
1
2
3
4
Clock cycle 5
6
7
8
9
lw $t0, 4($sp)
sub $v0, $a0, $a1 and $t1, $t2, $t3 or $s0, $s1, $s2 add $sp, $sp, -4
filling full emptying
IF | ID | EX | MEM | WB |  |  |  | 
 | IF | ID | EX | MEM | WB |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | IF | ID | EX | MEM | WB | 
 |  |  |  | IF | ID | EX | MEM | WB

## Slide 23: Visualizing Pipeline: Execution time
1
2
3
4
Clock cycle 5
6
7
8
9
lw $t0, 4($sp)
sub $v0, $a0, $a1 and $t1, $t2, $t3 or $s0, $s1, $s2 add $sp, $sp, -4
filling full emptying
IF | ID | EX | MEM | WB |  |  |  | 
 | IF | ID | EX | MEM | WB |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | IF | ID | EX | MEM | WB | 
 |  |  |  | IF | ID | EX | MEM | WB
first instruction: K cycles
Next N-1 instructions: N-1 cycles, total = K + (N-1) cycles
For a k-stage pipeline executing N instructions

## Slide 24: Pipelined versus Single cycle CPU design
Instruction | Ifetch | Decode | Execute | Memory | Writeback | Total time
LOAD | 200ns | 100 | 200 | 200 | 100 | 800ns
STORE | 200 | 100 | 200 | 200 |  | 700ns
ADD | 200 | 100 | 200 |  | 100 | 600ns
BRANCH | 200 | 100 | 200 |  |  | 500ns
Total latency in single cycle CPU: 3200 ns
Total latency in pipelined CPU (200ns clock cycle):
1000ns (1st instruction) + 3 X 200 ns (for next three) = 1600 ns

## Slide 25: What’s the big deal
Speedup = 3200ns/1600ns = 2X
What if we have a billion instructions?
Single cycle = 1 billion X 800ns = 800 seconds
Pipelined = 1000ns + (1 billion -1) X 200ns ~ 200 seconds
Speedup = 4X 

## Slide 26: Let’s include latch latency too
Inter-stage latch = 10ns
New clock cycle time in the pipelined design = 210ns
First instruction will get completed by 1040ns (five stages X 200 ns + four inter-stage latches X 10ns)
New Speedup = 800s/210s ~ 3.8X

## Slide 27: How to Divide the Datapath?
Suppose memory is significantly slower than other stages. For example, suppose
t
t
t
t
t
IM
DM
ALU
RF
RW
= 10 units
= 10 units
= 5 units
= 1 unit
= 1 unit
Since the slowest stage determines the clock, it may be possible to combine some stages without any loss of performance

## Slide 28: #Stages and Speedup
IM DM
1. t = t = 10,
tALU = 5,
tRF = tRW= 1
4-stage pipeline
Assumptions
Unpipelined
tC
Pipelined Speedup
tC
27
10
2.7
25
10
2.5
25
5
5.0
2. tIM =tDM = tALU = tRF = tRW = 5
4-stage pipeline
3. tIM =tDM = tALU = tRF = tRW = 5
5-stage pipeline

## Slide 29: Devil is in the details

## Slide 30: Stage-1: Fetch
Instruction bits
IF / ID
Pipeline register
Instruction Memory
PC
en
en
4
+
M
U X
PC + 4
Decode
target

## Slide 31: Stage 2: Decode
ID / EX
Pipeline register
regA contents
regB
Register File
regA regB
en
Instruction bits
IF / ID
Pipeline register
PC + 4
PC + 4
Control
Signals contents
Fetch
Execute
destReg
data
target

## Slide 32: Stage 3: Execute
ID / EX
Pipeline register
regA contents
regB contents
ALU
result
EX/Mem
Pipeline register
PC + 4
Control Signals
Control Signals
PC+4
+offset
+
regB contents
A L U
M U X
Decode
Memory
destReg
data

## Slide 33: Stage 4: Memory Stage
ALU
result
ALU
result
Control signals
PC+4
+offset
regB contents
Loaded
data
Control
signals
Execute
Write-back
in_addr
in_data
Data Memory
en R/W
destReg
data
target
EX/Mem
Pipeline register
Mem/WB Pipeline register

## Slide 34: Stage 5: Write-back
ALU
result
Mem/WB Pipeline register
Control signals
Loaded data
M U X
data
destReg
M U X
Memory

## Slide 35: The Complete Picture
PC
Inst
Mem
Register
File
X
A L
U
4
Data
Memory
+
M
U X
IF/ID
EX/Mem
Mem/WB
M U X
dest op ID/EX
offset
valB
valA
PC+4
PC+4
+ target
ALU
result
dest
op
valB
dest
op
ALU
M
result U
mdata
eq?
instruction
regA
regB
data
dest
M U X
data dest

## Slide 36: Coffee Credits
Aditya Agarwal