## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 13: Data/Control Hazards
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: The ideal world
Uniform Sub-operations
  Operation (op) can be partitioned into uniform-latency sub-ops
Repetition of Identical Operations
  Same ops performed on many different inputs
Independent Operations
  All ops are mutually independent

## Slide 3: The real world
Uniform Sub-operations NO
  Operation can be partitioned into uniform-latency sub-ops
Repetition of Identical Operations NO
  Same ops performed on many different inputs
Independent Operations NO
  All ops are mutually independent

## Slide 4: Structural/Data/Control Hazards
What is a hazard ? Anything that prevents an instruction to move ahead in the pipeline.
Structural: Resource conflicts, two instructions want to access the same structure on the same clock cycle.

## Slide 5: An Example with unified (single) memory
M
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
M
Reg
M
Reg
ALU
M
Reg
M
Reg
ALU
M
Reg
M
Reg
ALU
Reg
M
Reg
ALU
M
Reg
M
Reg
Can’t read same memory twice in same clock cycle

## Slide 6: What about registers?
M
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
M
Reg
M
Reg
ALU
M
Reg
M
Reg
ALU
M
Reg
M
Reg
ALU
Reg
M
Reg
ALU
M
Reg
M
Reg
Can read/write the register file (same register) in same clock cycle  but.. Real picture is different
Remember: Edge-triggered
Structural hazards are highly infrequent

## Slide 7: Data Hazards
Instruction depends on the result (data) of previous instruction(s).
Hazards happen because of data dependences.

## Slide 8: Data dependences (hazards)
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
read-after-write
(RAW)
True dependence

## Slide 9: Data dependences (hazards)
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
read-after-write
(RAW)
write-after-read
(WAR)
True dependence
anti dependence

## Slide 10: Data dependences (hazards)
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
read-after-write
(RAW)
write-after-read
(WAR)
write-after-write
(WAW)
True dependence
anti dependence
output dependence

## Slide 11: Data Hazards
  Read-After-Write (RAW)
    Read must wait until earlier write finishes
  Anti-Dependence (WAR)
    Write must wait until earlier read finishes
  Output Dependence (WAW)
    Earlier write can’t overwrite later write
    (WAW hazard: not possible with vanilla 5-stage pipeline)

## Slide 12: Data Hazards (Examples)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)

## Slide 13: Control Hazards
Hazards that arise from branch/jump instructions and any instructions that change the PC.

## Slide 14: An Example
What do you do with the 3 instructions in between?
How do you do it?
10: beq r1,r3,36
14: and r2,r3,r5 
18: or r6,r1,r7 
22: add r8,r1,r9 
50: xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 15: What happens on a hazard?
Instruction cannot move forward
Instruction must wait to get the hazard resolved.
The pipeline must stall 
It is like air bubbles in pipelines

## Slide 16: Stall/Bubble
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Stall
Instr 3
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Bubble
Bubble
Bubble
Bubble
Bubble
De-assert all control signals

## Slide 17: How to implement a stall?
Imm
IR
PC
we
addr
rdata
wdata
Ext
stall?
0x4
Add
nop
we
rs1
rs2
rd1
ws
wd rd2
ALU
we
addr
Memory
fetch
phase
GPRs
execute phase
rdata
Memory
wdata
Don’t fetch a new instruction and don’t change the PC
insert a nop (compiler way)

## Slide 18: An example of an NOP
sll $0 $0 (in MIPS)

## Slide 19: Simple Example (no bubbles)
add r3, r2, r1
add r6, r5, r4
C1 C2 C3 C4 C5 C6 C7 C8
IF1 ID1 IE1 IM1 IWB1
IF2 ID2 IE2 IM2 IWB2

## Slide 20: Simple Example (2 bubbles)
add r3, r2, r1
add r6, r5, r3
C1 C2 C3 C4 C5 C6 C7 C8
IF1 ID1 IE1 IM1 IWB1
IF2 ID2 ID2 ID2 IE2 IM2 IWB2

## Slide 21: Control Hazard and NOPs
I4 I5
 |  | time |  |  |  |  |  | 
 |  | t0 | t1 | t2 | t3 | t4 | t5 t6 | t7 . . . .
Resource Usage | IF ID EX MA WB | I1 | I2 I1 | I3 I2 I1 | I4 nop I2 I1 | I5 I4 nop I2 I1 | I5 nop I4 I2 nop nop  | I5 I4 I5 pipeline bubble
time
t0 t1
IF1 ID1 IF2
t7 . . . .
t2 t3 t4 t5 t6 EX1 MA1 WB1
ID2 EX2 MA2 WB2
IF3 nop nop nop nop
IF4 ID4 EX4 MA4 WB4
(I1) 096: ADD
(I2) 100: J 200
(I3) 104: ADD
(I4) 304: ADD

## Slide 22: What happens to the speedup?
Speedup = CPI unpipelined = CPI unpipelined
---------------------- -------------------------------------
CPI pipelined ideal CPI + stalls/instructions
Ideal CPI=1, assume stages are perfectly balanced

## Slide 23: Data Hazard Detector and stalls
Execute to decode:
EX/MEM.RegisterRd = ID/EX.RegisterRs
EX/MEM.RegisterRd = ID/EX.RegisterRt
Memory to decode:
MEM/WB.RegisterRd = ID/EX.RegisterRs
MEM/WB.RegisterRd = ID/EX.RegisterRt
what about instructions that do not write into the registers?

## Slide 24: Bypassing
Route data as soon as possible after it is calculated to the earlier pipeline stage

## Slide 25: Bypassing/forwarding: Updated Datapath
MEM/WR
ID/EX
EX/MEM
Data
Memory
ALU
mux
mux
Registers
NextPC
Immediate
mux

## Slide 26: How does it help?
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
lw r4, 0(r1)
sw r4,12(r1)
or r8,r6,r9
xor r10,r9,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 27: Does it help always?
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
or r8,r1,r9
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg