## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 14: Mitigating Control Hazards
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: What and Where? Control Hazard
What do we need to calculate next PC?
For Jumps
Opcode, offset, and PC
For Jump Register
Opcode and register value
For Conditional Branches
Opcode, offset, PC, and register (for condition)
For all others
Opcode and PC
In what stage do we know these?
PC - Fetch
Opcode, offset - Decode (or Fetch?)
Register value - Decode
Branch condition ((rs)==0) - Execute (or Decode?)

## Slide 3: Speculate, PC=PC+4
I
2
I1
104
PC
addr
inst
Inst
Memory
kill
PCSrc (pc+4 / target)
stall
Add
E M
0x4
Add
nop
IR IR
Jump?
IR
I1
I2
I3
I4
096 ADD
100 J304
104 ADD
304 ADD
What happens on mis-speculation, i.e., when next instruction is not PC+4?
How? Insert NOPs

## Slide 4: Conditional branches
I1
I2
I3
I4
096 ADD
100 BEQZ r1 200
104 ADD
304 ADD
Branch condition is not known
until the execute stage
Instructions between a branch instruction and the target are
in the wrong-path if the branch is not taken

## Slide 5: Again (stalls/NOPs)
time
t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) 096: ADD IF1 ID1
EX1
MA1 WB1
(I2) 100: BEQZ 200 IF2
ID
2
EX2 MA2
WB2
(I3) 104: ADD IF3
ID3 nop nop nop
(I4)
108:
IF4 nop nop nop nop
(I5)
304: ADD
IF5
ID5 EX5 MA5 WB5
time
t0 t1 t2 t3 t4 t5 t6 t7 . . . .
Resource
Usage
IF I1 I2 ID I1
EX
MA
WB
I3
I2
I1
I4
I3
I2
I1
I5
nop I5
nop nop I5
I2 nop nop I5
I1
I2 nop nop I5

## Slide 6: Branches: Taken/Not Taken and Target
Instruction Taken known? Target known?
J
After Inst. Decode After Inst. Decode
BEQZ/BNEZ
After Inst. Execute After Inst. Execute
what action should be taken in the decode stage?
Can we add an ALU in the decode stage?

## Slide 7: What else can be done? Compiler?
Delayed branch: Define branch to take place AFTER a following instruction(used to be in early RISC processors)
branch instruction
sequential successor1
sequential successor2
........
sequential successorn
branch target if taken
Branch delay of length n

## Slide 8: Scheduling Branch Delay Slots
A is the best choice, fills delay slot & reduces instruction count (IC)
add $1,$2,$3 if $2=0 then
delay slot
A. From before branch
becomes
if $2=0 then
add $1,$2,$3

## Slide 9: Scheduling Branch Delay Slots
A is the best choice, fills delay slot & reduces instruction count (IC)
add $1,$2,$3 if $2=0 then
delay slot
A. From before branch B. From branch target
add $1,$2,$3 if $1=0 then
delay slot
sub $4,$5,$6
becomes
becomes
if $2=0 then
add $1,$2,$3
add $1,$2,$3 if $1=0 then
sub $4,$5,$6

## Slide 10: Scheduling Branch Delay Slots
A is the best choice
add $1,$2,$3 if $2=0 then
delay slot
A. From before branch B. From branch target
add $1,$2,$3 if $1=0 then
delay slot
C. From fall through
add $1,$2,$3 if $1=0 then
delay slot
sub $4,$5,$6
sub $4,$5,$6
becomes
becomes
if $2=0 then
add $1,$2,$3
add $1,$2,$3 if $1=0 then
sub $4,$5,$6
becomes
add $1,$2,$3 if $1=0 then
sub $4,$5,$6

## Slide 11: Word of Caution!
Do not put a branch
in the branch delay slot 

## Slide 12: Stalls and Performance
For a program with N instructions and S stall cycles,
Average CPI = N
---------
N

## Slide 13: Stalls and Performance
For a program with N instructions and S stall cycles,
Average CPI = N+S
---------
N

## Slide 14: New Pipeline Speedup
Pipeline Speedup = Pipeline Depth
----------------------------------------------------
1+pipeline stalls because of branches
Pipeline stalls (branches) = Branch frequency X penalty

## Slide 15: Summary
Data Hazards
Bypassing/forwarding
Stalls (NOPs) – if no scope for bypassing
Control hazards
Speculate, PC=PC+4, kill the wrong path
Delayed branch with the help of branch delay slots, new pipeline speedup

## Slide 16: Branch instructions
I1:
I2:
I3:
I4:
I5:
t1
t2
t3
t4
t5
t6
t7
t8
Time:
Inst
I6:
IF (Fetch)
ID (Decode)
EX (ALU)
MEM
WB
IF
ID
IF
EX
ID
IF
MEM
WB
EX stage computes if branch is taken
If branch is taken, these instructions MUST NOT complete!
I-Mem

## Slide 17: Branch Predictors
I1:
I2:
I3:
I4:
I5:
t1
t2
t3
t4
t5
t6
t7
t8
Time:
Inst
I6:
IF (Fetch)
ID (Decode)
EX (ALU)
MEM
WB
IF
ID
IF
EX
ID
IF
MEM
WB
EX stage computes if branch is taken
If branch is taken, these instructions MUST NOT complete!
I-Mem
A control instr?
Taken or Not Taken?
If taken, where to? What PC?
Branch Predictor
Predictions

## Slide 18: A quick recap
What if PC=PC+4? Not TRUE
Flush/kill all the instructions in the wrong path.

## Slide 19: Branch Prediction: 10K Feet View
Predict whether the next PC is a branch PC, at the fetch stage?

## Slide 20: Branch Prediction: 10K Feet View
Predict whether the next PC is a branch PC, at the fetch stage?
If branch, will it be taken?

## Slide 21: Branch Prediction: 10K Feet View
Predict whether the next PC is a branch PC, at the fetch stage?
If branch, will it be taken?
If taken, what is the target address?

## Slide 22: Branch Prediction: 10K Feet View
Predict whether the next PC is a branch PC, at the fetch stage?
If branch, will it be taken?
If taken, what is the target address?
How?

## Slide 23: Branch Prediction: 10K Feet View
Predict whether the next PC is a branch PC, at the fetch stage?
If branch, will it be taken?
If taken, what is the target address?
How?
We know whether it is a branch PC or not in the decode stage. Oh no 

## Slide 24: Branch Predictor: A bit deeper
Three tasks
Is the PC a branch/jump? YES/NO
If Yes, can we predict the direction? Taken or not-taken
If taken, can we predict the target address?

## Slide 25: Let’s see
Program
Counter
Address of the
current branch

## Slide 26: Let’s see
Direction predictor
Program
Counter
PC + 4
taken?
Next Fetch
Address
Address of the
current branch

## Slide 27: Let’s see
target address
Direction predictor
Repository of Target Addresses (BTB: Branch Target Buffer)
Program
Counter
PC + 4
taken?
Next Fetch
Address
hit?
Address of the
current branch

## Slide 28: Static (compiler) Direction Prediction Techniques
Always not-taken: Simple to implement: no need for BTB,
no direction prediction
Low accuracy: ~30-40%
Always taken: No direction prediction, we need BTB though
Better accuracy: ~60-70%
Backward branches (i.e., loop branches) are usually taken

## Slide 29: Dynamic Predictors
Microarchitectural way of predicting it.
Simple one: Last time predictor

## Slide 30: Last-time predictor
predict
taken
predict
not
taken
actually
taken
actually
not taken

## Slide 31: Last-time predictor
predict
taken
predict
not
taken
actually
not taken
actually
taken
actually
taken
actually
not taken

## Slide 32: Implementation
K bits of branch instruction address
Index

## Slide 33: Implementation
K bits of branch instruction address
Index
Branch history table of 2K entries, 1 bit per entry

## Slide 34: Implementation
K bits of branch instruction address
Index
Branch history table of 2K entries, 1 bit per entry
Use this entry to predict this branch:
0: predict not taken
1: predict taken

## Slide 35: Performance of Last-time predictor
TTTTTTTTTTNNNNNNNNNN - 90% accuracy
Always mispredicts the last iteration and the first iteration of a loop branch
Accuracy for a loop with N iterations = (N-2)/N
+ Loop branches for loops with large number of iterations
-- Loop branches for loops will small number of iterations

## Slide 36: Performance contd.
TNTNTNTNTNTNTNTNTNTN  0% accuracy
20% of all instructions are branches, 85% accuracy
Last-time predictor CPI =
[ 1 + (0.20*0.15) * 2 ] =
1.06 (minimum two stalls to resolve a branch)