## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 15: Branch Prediction and Interrupts/Exceptions
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: 2-bit Bimodal Predictors: A bit better
pred
Taken
11
pred
Taken
10
pred
!taken
01
pred
!taken
00
actually
taken
actually
taken
actually
!taken
actually
!taken
actually
!taken
actually
!taken
actually
taken
actually
taken
2-bit saturating counter:
Values from 00 to 11
Counter greater than
equal to 10,
prediction: taken

## Slide 4: No history predictor: 2 bit predictor
k bit
2p
(PC >> 2) &
(2p -1)
Bimodal predictor: Good for biased branches

## Slide 5: Local and global history
Local Behavior
  What is the predicted direction of Branch A given the outcomes of previous instances of Branch A ?
Global Behavior
What is the predicted direction of Branch Z given the outcomes of all* previous branches A, B, …, X and Y?
Number of previous branches tracked limited by the history length

## Slide 6: Two Level Branch Predictors
First level: Global branch history register (N bits)
  The direction of last N branches
Second level: Table of saturating counters for each history entry
  The direction the branch took the last time the same history was seen
1 1 ….. 1 0
GHR
(global history register)

## Slide 7: Two Level Branch Predictors
First level: Global branch history register (N bits)
  The direction of last N branches
Second level: Table of saturating counters for each history entry
The direction the branch took the last time the same history was seen
1 1 ….. 1 0
GHR
(global history register)
00 …. 00
00 …. 01
00 …. 10
11 …. 11
index
Pattern History Table (PHT)
previous one

## Slide 8: Two Level Branch Predictors
First level: Global branch history register (N bits)
  The direction of last N branches
Second level: Table of saturating counters for each history entry
The direction the branch took the last time the same history was seen
1 1 ….. 1 0
GHR
(global history register)
00 …. 00
00 …. 01
00 …. 10
11 …. 11
0
1
2
3
index
Pattern History Table (PHT)
previous one

## Slide 9: GHR per branch
1 1 ….. 1 0
00 …. 00
00 …. 01
00 …. 10
11 …. 11
m bit
k bit
2m
2p
(PC >> 2) &
(2p -1)
BHT
PHT
Mostly K=2, m =12 for example
BHT: Branch history table

## Slide 10: Set of branches: One register for correlated ones
1 1 ….. 1 0
m bit
2p
(PC %
2p )
BHT
Can lead to positive/negative/neutral interference
00 …. 00
00 …. 01
00 …. 10
11 …. 11
k bit
2m
PHT
B1: if (aa == 2) aa = 0;
B2: if (bb == 2); bb=0;
B3: if (aa != bb) { … }

## Slide 11: Gshare is the answer
1 1 ….. 1 0
00 …. 00
00 …. 01
00 …. 10
11 …. 11
m bit
k bit
2m
PC >>2 & 2m -1
For a given history and for a given branch (PC) counters are trained

## Slide 12: Few Important Points
Branch prediction happens at the IF stage.
We know the target outcome at the end of EX stage.
So BHT and PHT will be updated after EX stage for the corresponding PC. Any issues here?

## Slide 13: Issue
I1 F D E
I2 F D E
I3 F D E
Lets assume I1 and I3 are branch instructions. I1 will update BHT and PHT in E stage, and I3 will probe BHT and PHT in F stage. To make sure PHT is updated correctly with the correct BHT entry, BHT entry is communicated till the E stage.

## Slide 14: State-of-the-art

## Slide 15: BTB (Target Address Predictor)
0b0110[...]01001000
2 state bits
Branch
History Table
(BHT)
target address
Branch Target Buffer (BTB)
PC + 4 + Loop
30-bit address tag
0b0110[...]0010
Address of branch instruction
BTB is probed in the fetch stage along with the direction predictor.
A hit in the BTB means the PC is a branch PC.
Branch instruction
BNEZ R1 Loop

## Slide 16: Exception/Interrupt
An unscheduled event that disrupts program (instructions) in action.

## Slide 17: Interrupt Handling
Ii-1
HI1
HI2
HIn
Ii
Ii+1
program
interrupt
handler
An external or internal event that needs to be processed. The event is usually unexpected or rare from program’s point of view.

## Slide 18: Causes
Asynchronous: an external event
  input/output device service-request
  timer expiration
  power disruptions, hardware failure
Synchronous: an internal event (a.k.a. traps or exceptions)
  undefined opcode, privileged instruction
  arithmetic overflow, FPU exception, misaligned memory access
  virtual memory exceptions: page faults, TLB misses, protection violations
  system calls, e.g., jumps into kernel

## Slide 19: Interrupt and Exception

## Slide 20: Interrupt Handler
Exception program counter (EPC): address of the offending instruction,
Saves EPC before enabling interrupts to allow nested interrupts
Need to mask further interrupts at least until EPC can be saved
Need to read a status register that indicates the cause of the interrupt

## Slide 21: Handshake between processor and the OS
Processor:
stops the offending instruction,
makes sure all prior instructions complete,
flushes all the future instructions (in the pipeline)
Sets a register to show the cause
Saves EPC
Jumps to pre-decided address (cause register or vectored)
Disables further interrupts

## Slide 22: Handshake between processor and the OS
OS:
Looks at the cause of the exception
Handles the interrupt/exception
Interrupt handler saves the GPRs
Calls RFE

## Slide 23: Contd.
Uses a special indirect jump instruction RFE (return-from-exception) which
  enables interrupts
  restores the processor to the user mode