## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 16: Beyond scalar and performance evaluation
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Exception handling and Pipelining
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous Interrupts
When do we stop the pipeline for precise interrupts or exceptions?
How to handle multiple simultaneous exceptions in different pipeline stages?
How and where to handle external asynchronous interrupts?
Nothing can happen
now?

## Slide 3: Contd.
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous
Interrupts
Exc
D
PC
D
Exc
E
PC
E
Exc
M
PC
M
Cause
EPC
Kill D Stage
Kill F Stage
Kill E Stage
Select Handler PC
Kill Writeback
Commit Point

## Slide 4: Contd.
Hold exception flags in pipeline until commit point for instructions that will be killed
Exceptions in earlier pipe stages override later exceptions for a given instruction
If exception at commit: update cause and EPC registers, kill all stages, inject handler PC into fetch stage

## Slide 5: Moving on in the pursuit of IPC++

## Slide 6: Beyond Scalar
Scalar pipeline limited to CPI ≥ 1.0
  Can never run more than 1 insn per cycle
“Superscalar” can achieve CPI ≤ 1.0 (i.e., IPC ≥ 1.0)
  Superscalar means executing multiple insns in parallel

## Slide 7: Instruction Level Parallelism (ILP)
Scalar pipeline (baseline)
  Instruction overlap parallelism = D
  Peak IPC = 1.0
D
Successive
Instructions
Time in cycles
1
2
3
4
5
6
7
8
9
10
11
12
D different instructions overlapped

## Slide 8: Superscalar Processor
Superscalar (pipelined) Execution
  Instruction parallelism = D x N
  Peak IPC = N per cycle
Successive
Instructions
Time in cycles
1
2
3
4
5
6
7
8
9
10
11
12
N
D x N different instructions overlapped

## Slide 9: What is the deal?
We get an IPC boost if the number of instructions fetched in one cycle are independent 
Complicates datapaths, multi-ported structures, complicates exception handling

## Slide 10: Out of order (O3) processor: Pursuit of even higher IPC

## Slide 11: Out-of-order follows data-flow order
Example:
(1) r1  r4 / r7 (2) r8  r1 + r2
(3) r5  r5 + 1 (4) r6  r6 - r3 (5) r4  r5 + r6 (6) r7  r8 * r4
/* assume division takes 20 cycles */
1 | 2 | 3 | 4 | 5 | 6
In-order execution
1 |  |  |  | 
3 | 5 |  | 2 | 6
4 |  |  |  | 
Out-of-order execution
2
5
Data Flow Graph
1 3 4
r1 r5 r6
r8 r4
6
1 | 2 | 4 | 5 | 6
 | 3 |  |  | 
In-order (2-way superscalar)

## Slide 12: O3
Two or more instructions can execute in any order if they have no dependences (RAW, WAW, WAR)
Completely orthogonal to superscalar/pipelining

## Slide 13: O3 + Superscalar
In-order Instruction Fetch
(Multiple fetch in one cycle)
1. LOAD
3. LOAD
4. LOAD
5. MUL
2. SUB

## Slide 14: O3 + Superscalar
In-order Instruction Fetch
(Multiple fetch in one cycle)
1. LOAD
3. LOAD
4. LOAD
5. MUL
2. SUB
300 cycles
30 cycles
5 cycles 
1 cycle 
2 cycles 
Out-of-order execution

## Slide 15: O3 + Superscalar
In-order Instruction Fetch
(Multiple fetch in one cycle)
1. LOAD
3. LOAD
4. LOAD
5. MUL
2. SUB
300 cycles
30 cycles
5 cycles 
1 cycle 
2 cycles 
1. LOAD
3. LOAD 
4. LOAD 
5. MUL
2. SUB 
In-order Commit
Out-of-order execution

## Slide 16: The Big Picture
Program Form
Processing Phase
Static program
dynamic inst.
Stream (trace)
execution
window
completed
instructions
Dispatch/ dependences
inst. Issue
inst execution
inst. Reorder &
commit

## Slide 17: The notion of Commit
After commit, the results of a committed instruction is visible to the programmer
and
the order at which instructions are fetched is also visible.

## Slide 18: Why we need in-order commit?
Think about exceptions and precise exceptions
We should know till when we are done as per the programmer’s view.

## Slide 19: Quantifying Performance

## Slide 20: Performance: Time (Iron Law)
Time/Program =
Instructions/program X cycles/instruction X Time/cycle
Source code ISA microarch.
Compiler microarch. technology
ISA

## Slide 21: Performance: Time (Iron Law)
Time/Program =
Instructions/program X cycles/instruction X Time/cycle
(∑ IC(i) X CPI (i)) X Time/cycle

## Slide 22: Example
Program p = one billion instructions
Processor takes one cycle per instruction
Processor clock is 1GHz
CPU time = 109 instructions X 1 cycle/instruction X 1 ns
= 1 second

## Slide 23: Example
Program p = one billion instructions
Processor takes one cycle per instruction
Processor clock is 4 GHz
CPU time = 109 instructions X 1 cycle/instruction X 1/4 ns
= 0.25 second (4X faster)

## Slide 24: Example
Program p = one billion instructions
Processor processes 10 instructions in one cycle
Processor clock is 4 GHz
CPU time = 109 instructions X 0.10 cycle/instruction X 1/4 ns
= 0.025 second (40X faster)

## Slide 25: Example (Role of compiler/programmer)
Program p = one million instructions
Processor processes 1 instruction in one cycle
Processor clock is 4 GHz
CPU time = 106 instructions X 1 cycle/instruction X 1/4 ns
= 0.00025 second (4000X faster)

## Slide 26: A bit deeper
Program p has 10 billion instructions
* 2 billion branches (CPI of 4)
* 3 billion Loads (CPI of 2)
* 1 billion Stores (CPI of 3)
* Rest 4 billion, arithmetic instructions ( CPI of 1)
Clock rate 4GHz, What is the execution time?

## Slide 27: Which one ?
Processor IMTEL: CPI 2, Clock rate 2GHz
Processor AND: CPI 1, Clock rate 1GHz
Assume compiler/ISA/… are the same.
IMTEL: 2 X 0.5 ns = 1 ns per instruction
AND: 1 X 1ns = 1ns per instruction 

## Slide 28: Empirical Evaluation
Benchmarks
Metrics
Latency and bandwidth
Simulators