## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 17: Empirical evaluation and Memory Hierarchy
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Empirical Evaluation
Benchmarks
Metrics
Latency and bandwidth
Simulators

## Slide 3: Performance
3
• Latency (execution/response time): time to finish one task. It is additive (Performance = 1/latency)
• Throughput (bandwidth): number of tasks/unit time. It is not additive
• Latency lags bandwidth, Bandwidth hurts latency,
Read: https://cacm.acm.org/magazines/2004/10/6401-latency-lags-bandwith/fulltext

## Slide 4: Latency vs bandwidth
Latency vs Bandwidth, How they affect each other?
Latency helps bandwidth but not vice versa.
DRAM latency
More # Accesses ~DRAM Bandwidth
Bandwidth usually hurts latency
Queues - Bandwidth
Increases latency

## Slide 5: For the curious ones
Bandwidth problems can be cured with money.
Latency problems are harder because the speed of light is fixed – you can’t bribe God
https://www.youtube.com/watch?list=PL2LuePcZTMh_MzNHqZWNdvWdAnAThHCKK&v=lfqgpuH10uc&feature=emb_logo
https://www.youtube.com/watch?v=GNK-67JUH7M&list=PL2LuePcZTMh_MzNHqZWNdvWdAnAThHCKK&index=2
https://www.youtube.com/watch?v=5CxpoGwCxKU&list=PL2LuePcZTMh_MzNHqZWNdvWdAnAThHCKK&index=3
Some of the major bottlenecks: latency and bandwidth bottlenecks

## Slide 6: Amdahl’s Law (common case fast)
Speedup overall
Execution Time old
-------------------------------------------
Execution Time new
=
=
1
---------------------------------------------------------------------------------------
(1 – Fraction enhanced) + Fraction enhanced
------------------------------------
Speedup
enhanced

## Slide 7: Amdahl’s Law
Which one will provide better overall speedup?
Small speedup on the large fraction of execution time.
Large speedup on the small fraction of execution time.
Does not matter.
Depends on the difference between small and large. Mostly it is A.

## Slide 8: Evaluation
To compare Processor A with Processor B by running programs
How many programs?
The programs that you care.
What if I want to build a new one (processor, caches, DRAM) ?

## Slide 9: World of Benchmarks
SPEC CPU 2017 (https://www.spec.org/cpu2017/)
The SPEC CPU® 2017 benchmark package contains SPEC's next-generation, industry-standardized, CPU intensive suites for measuring and comparing compute intensive performance, stressing a system's processor, memory subsystem and compiler.
SPECspeed: used for comparing time for a computer to complete single tasks
SPECrate: measure the throughput or work per unit of time.

## Slide 10: World of Benchmarks
CloudSuite (https://www.cloudsuite.ch/)
CloudSuite is a benchmark suite for cloud services. The benchmarks are based on real-world software stacks and represent real-world setups.
PARSEC (https://parsec.cs.princeton.edu/)
Benchmark suite composed of multithreaded programs. The suite focuses on emerging workloads and was designed to be representative of next-generation shared-memory programs for chip-multiprocessors.

## Slide 11: World of Benchmarks
MobileBench (https://mobilebench.engineering.asu.edu/)
comprising a selection of representative smart phone applications.
Many more application domain specific: Graph processing, ML perf,

## Slide 12: Pitfalls of Benchmarks
Benchmark not representative of all
Your workload is I/O bound → SPECCPU is useless
Benchmark is too old
Need to be periodically refreshed

## Slide 13: Non-benchmarks
Application kernels: A small code fragment or part of the program
Synthetic benchmark : Not part of any real program!!
Micro-benchmark
OK! So, I will create a chip and then evaluate these benchmarks

## Slide 14: World of Simulators
Functional Simulator: Used to verify the correct execution of the program. Can not be used for performance evaluation.
Performance simulators:
Trace-driven: ChampSim (https://github.com/ChampSim/ChampSim)
Execution-driven: gem5, Multi2sim
Functional simulator is part of the performance simulators.

## Slide 15: Evaluation Continued
Pick a relevant benchmark suite
Measure IPC of each program
Summarize the performance using:
Arithmetic Mean (AM)
Geometric Mean (GM)
Harmonic Mean (HM)
Which one to choose?

## Slide 16: Example
IMTEL
ABM
AND
App. one
App. two
App. three
10
20
30
20
30
40
30
40
10
Which machine performs better over IMTEL and why?

## Slide 17: Contd.
ABM
AND
App. one
App. two
App. three
2
3
1.5
2
1.3
0.3
A.M.
1.60
1.76
G.M.
1.57
1.21
H.M.
1.54
0.72

## Slide 18: AM on ratios (use always GM on ratios)
 | X | Y
App. 1 | 1 | 100
App. 2 | 1000 | 10
Normalized to X | X | Y
App. 1 | 1 | 100
App. 2 | 1 | 0.01
AM | 1 | 50.005
Normalized to Y | X | Y
App. 1 | 0.01 | 1
App. 2 | 100 | 1
AM | 50.005 | 1
Y is 50 times faster than X
X is 50 times faster than Y

## Slide 19: Time for Memory Hierarchy

## Slide 20: The Ideal World
Instruction
Supply
(Fetch stage)
Pipeline
(Instruction
execution)
Data
Supply
(Memory stage)
- Zero-cycle latency
- Infinite capacity
- Perfect control flow
Zero-cycle latency
Infinite capacity
- Infinite bandwidth

## Slide 21: World of Memory Hierarchy: Why?
Before that What is memory?

## Slide 22: Semiconductor Memory
Semiconductor memory began to be competitive in early 1970s
  Intel formed to exploit market for semiconductor memory
  Early semiconductor memory was Static RAM (SRAM). SRAM cell internals similar to a latch (cross-coupled inverters).
First commercial Dynamic RAM (DRAM) was Intel 1103
  1Kbit of storage on single chip
  charge on a capacitor used to hold value

## Slide 23: One transistor DRAM
1-T DRAM Cell
word
bit
access transistor
Storage
capacitor
VREF
Denser
Value kept in one cell is as
per the charge in the capacitor
Need to be refreshed periodically to maintain the charge
So dynamic RAM (DRAM)

## Slide 24: DRAM
Dynamic random-access memory
Capacitor charge state indicates stored value
  Whether the capacitor is charged or discharged indicates storage of 1 or 0
  1 capacitor
  1 access transistor
Capacitor leaks
  DRAM cell loses charge over time
  DRAM cell needs to be refreshed

## Slide 25: SRAMs (6T to 8T)
Static RAMs. No need of refresh as no capacitor.
Faster access (no capacitor)
Density low as 6T: 1 bit compared to 1T: 1bit in DRAM
Costly than DRAM

## Slide 26: The Problem
Bigger is slower
  SRAM, 512 Bytes, sub-nanosec
  SRAM, KByte~MByte, ~nanosec
  DRAM, Gigabyte, ~50 nanosec
  Hard Disk, Terabyte, ~10 millisec
Faster is more expensive (dollars and chip area)
  SRAM, < 1000$ per GB
  DRAM, < 20$ per GB
  Hard Disk < 0.01$ per GB
  These sample values scale with time
Other technologies have their place as well
  Flash memory, NVRAM, MRAM etc

## Slide 27: Size affects latency
Small Memory
CPU
Big Memory
CPU
Signals have further to travel
Fan out to more locations

## Slide 28: Why Memory Hierarchy
We want both fast and large
But we cannot achieve both with a single level of memory
Idea: Have multiple levels of storage (progressively bigger and slower as the levels are farther from the processor) and ensure most of the data the processor needs is kept in the fast(er) level(s)

## Slide 29: Welcome to Memory Hierarchy
Small,
Fast Memory
(RF, SRAM)
capacity: Register << SRAM (Cache) << DRAM
latency: Register << SRAM (Cache) << DRAM
bandwidth: on-chip >> off-chip
On a data access:
  if data Î fast memory  low latency access Cache
  if data Ï fast memory  high latency access DRAM
CPU
Big, Slow Memory
(DRAM)
A
B
holds frequently used data

## Slide 30: World with no caches
Costly DRAM accesses
200 to 300 cycles
Core
Minimizing costly DRAM accesses is critical for performance
South pole 
North pole 
32-bit Address
Data
4 GB DRAM