## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 18: Cash, no; Caches
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: World with no caches
Costly DRAM accesses
200 to 300 cycles
Core
Minimizing costly DRAM accesses is critical for performance
South pole 
North pole 
32-bit Address
Data
4 GB DRAM

## Slide 3: Remember Latency and Bandwidth
Core
Latency
Bandwidth

## Slide 4: Latency 
Bandwidth problems can be cured with money.
Latency problems are harder because the speed of light is fixed – you can’t bribe God

## Slide 5: Why access memory?
200 Cycles
DRAM Contr.
Core
CPU
Memory stores CODE and DATA
Processor accesses for LOADs (reads) and STOREs(writes)
Memory Wall: Grandmother of all the walls 

## Slide 6: Do not ignore the common case mantra
Reduction in DRAM accesses ~ Improvement in execution time
WRONG!
First Law of Performance:
  Make the common case fast
What if your program is not memory intensive

## Slide 7: Let’s look at the Applications (benchmarks)
Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)
Time
Memory Address (one dot per access)

## Slide 8: Oh Yes locality
Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)
Time
Memory Address (one dot per access)
Spatial
Locality
Temporal
Locality

## Slide 9: Few Examples
Address
Time
Instruction
fetches
Stack
accesses
Data
accesses
n loop iterations
subroutine call
subroutine return
argument access
vector access
scalar accesses

## Slide 10: Caching: 10K Feet View
Costly DRAM accesses
200 to 300 cycles
Core
North pole 
Address
Data
$
Address
Data
Caching is a speculation technique 
Works – if locality

## Slide 11: Caching: 10K Feet View
Costly DRAM accesses
200 to 300 cycles
Core
North pole 
Address
Data
$
Address
Data
Caching is a speculation technique 
Works – if locality

## Slide 12: How big/small?
$
$
Core
Latency: low
Area: low
Capacity: low
Latency: high
Area: high
Capacity: high

## Slide 13: 1K Feet View of an O3 core: A bit Deeper
In-order Instruction Fetch
(Multiple fetch in one cycle)
1. LOAD
3. LOAD
4. LOAD
5. MUL
2. SUB
1. LOAD 
3. LOAD 
4. LOAD 
5. MUL
2. SUB 
DRAM: 300 cycles
300 cycles
300 cycles
1 cycle 
2 cycles 
Bottleneck
Processor core says all LOADs should take one cycle. Ehh!

## Slide 14: Impact of one DRAM access
1. LOAD
3. LOAD
4. LOAD
2. SUB
DRAM: 100ns (16 instructions per ns)
.
.
.
4-fetch and issue processor running at 4GHz (0.25ns)

## Slide 15: Impact of one DRAM access
1. LOAD
3. LOAD
4. LOAD
2. SUB
DRAM: 100ns (16 instructions per ns)
.
.
.
4-fetch and issue processor running at 4GHz (0.25ns)
#instructions can get executed during one DRAM access: 1600  

## Slide 16: Cache with latency
Costly DRAM accesses
200 to 300 cycles
Core
South pole 
North pole 
Address
Data: 1 cycle
$
Address
Data
32 to 64KB $ will be available in one to four cycles 

## Slide 17: Cache hierarchy with latency
Core
South pole 
North pole 
Address
Data: 1 cycle
$
Address
10 cycles
Multi-level cache hierarchy
$
$
Address
30 cycles
10s of KBs
100s of KBs
1000s of KBs

## Slide 18: Cache hierarchy with latency
Core
South pole 
North pole 
Address
Data: 1 cycle
$
Address
10 cycles
Multi-level cache hierarchy
$
$
Address
30 cycles
10s of KBs
100s of KBs
1000s of KBs
How many levels ?
Total latency < DRAM latency

## Slide 19: Takeaway
L1 $
L2 $
L3 $
Latency and bandwidth (multiple ports)

## Slide 20: Takeaway
L1 $
L2 $
L3 $
Latency and bandwidth (multiple ports)
Latency

## Slide 21: Takeaway
L1 $
L2 $
L3 $
Latency and bandwidth (multiple ports)
Latency
Capacity

## Slide 22: Accessing a cache
Core
One byte

## Slide 23: Bytes to blocks (lines)
Core
One byte
One line
Typical line size: 64 to 128 Bytes

## Slide 24: A bit deeper: 1024 lines each of 32B
Core
One byte
Line 0
Address (32-bit)
4 GB DRAM
Line 1023
One line

## Slide 25: A bit deeper: 1024 lines each of 32B
Core
One byte
Line 0
Address (32-bit)
4 GB DRAM
Line 1023
One line
Line number (index): 10 bits
Byte offset (offset): 5 bits

## Slide 26: Direct Mapped Cache
Tag
Index
Offset
Line 0
Line 1023
Line 512
.
.
.
byte

## Slide 27: Direct Mapped in Action
:
0x50
Valid Bit
:
Cache Tag
Byte 32
0
1
2
3
:
Cache Data
Byte 0
Byte 1
Byte 31
:
Byte 33
Byte 63
:
Byte 992
Byte 1023
:
1023
Ex: 0x50
Ex: 0x00
Cache Index
0
5
31
Cache Tag
Byte Select
14
Ex: 0x01

## Slide 28: What if we have multiple ways?
One byte
Line 0
Line 1023
Set 0
Set 511
Tag
Index
Offset
byte
Tag
Tag
Tag
Tag

## Slide 29: 2-way associative in action
Cache Index
0
5
31
Cache Tag
Byte Select
14
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Mux
0
1
Sel1
Sel0
OR
Hit
Compare
Compare
Cache Block

## Slide 30: 4-way associative: Just a better picture
Data
Tag
V
0
1
2
.
.
.
255
Data
Tag
V
0
1
2
.
.
.
255
Data
Tag
V
0
1
2
.
.
.
255
Data
Tag
V
0
1
2
.
.
.
255
Index
Tag
Hit
Data
4x1 select

## Slide 31: Extreme: One cache, one set, fully associative
One byte
Line 0
Line 1023
Tag
Offset
byte
Tag
Tag
Tag
Tag

## Slide 32: A bit different way
Baker Street: Cache Index 
221b: Tag bits 
Sherlock Holmes: Byte offset  