## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 19: Caches-II
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Knobs of interest
Line size, associativity, cache size
Tradeoff: latency, complexity, energy/power
Tips: Think about the extremes:
Line size = one byte or cache size
Associativity = one or #lines
Cache size = Goal oriented: latency/bandwidth or capacity
https://github.com/HewlettPackard/cacti/

## Slide 3: Cache misses
Cold Miss: cache starts empty and this is the first reference
Conflict Miss: Many mapped to the same index bits
Capacity Miss: Cache size is not sufficient
Coherence Miss: in Multi-core systems, only [not I/O coherence]

## Slide 4: On a Miss, Replace a block, which block?
Think of each block in a set having a “priority”
  Indicating how important it is to keep the block in the cache
Key issue: How do you determine/adjust block priorities?
Ideally: Belady’s OPT policy, replace the block that will be used furthest in the future. No one knows the future though 
There are three key decisions in a set:
  Insertion, promotion, eviction (replacement)

## Slide 5: A simple LRU (Least-Recently-Used) Policy
Cache Eviction Policy: On a miss (block i), which block to evict (replace) ?
Cache Insertion Policy: New block i inserted into MRU.
Cache Promotion Policy: On a future hit (block i), promote to MRU
a
b
c
d
e
f
g
h
MRU
LRU
SET A
i
a
b
c
d
e
f
g
MRU
LRU
SET A
We need priority bits per block. For example, a 16-way cache will need four bit/block LRU causes thrashing when working set > cache size

## Slide 6: Types of Applications

## Slide 7: Let’s redefine cache misses
Compulsory: first reference to a line (a.k.a. cold start misses)
  misses that would occur even with infinite cache
Capacity: cache is too small to hold all data
  misses that would occur even under perfect (Belady’s) replacement policy
Conflict: misses that occur because of collisions due to line-placement strategy
  misses that would not occur with ideal full associativity

## Slide 8: Cache knobs and Misses
Larger cache size
  reduces capacity and conflict misses?
  hit time will increase
Higher associativity
  reduces conflict misses
  - increase hit time
Larger line size
  reduces compulsory misses
  increases conflict misses and miss penalty

## Slide 9: Line size
Too small blocks:
  don’t exploit spatial locality well
  have larger tag overhead
Too large blocks:
  too few total # of blocks
    likely-useless data transferred
    Extra bandwidth/energy consumed
Line size
Hits

## Slide 10: Cache size
hit rate
cache size
“working set” size
Working set: the whole set of data the executing application references within a time interval

## Slide 11: Associativity
hit rate
associativity
Myth: It should be power of two. NO!!
L1 cache: lower associativity, hit time
L3 cache: higher associativity