## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 20: Caches-III
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Cache Performance
How good is the cache for a given application?
Hit rate
Miss rate
Misses per kilo instructions (MPKI)
But Why?

## Slide 3: Average Access Time
On average, how much time it takes for a LOAD to complete
Average memory access time (AMAT) =
Hit time + Miss rate x Miss penalty
Hit time-L1 + Miss rate-L1 x Miss penalty-L1
Miss penalty-L1 = Hit time-L2 + Miss rate-L2 x Miss penalty-L2
Hit time: Low, Miss rate: Low , Miss penalty: Low
Ideally, miss rate = 0.00% and hit time should be one cycle, so all LOADs will take just one cycle 

## Slide 4: The Implications of L1-D Hit rate of 100%
1. LOAD
3. LOAD
4. LOAD
5. MUL
2. SUB
1. LOAD
3. LOAD 
4. LOAD 
5. MUL
2. SUB 
DRAM: 300 cycles
L3 Cache: 30 cycles
L1 Cache: 5 cycles 
1 cycle 
2 cycles 
Bottleneck

## Slide 5: A Dreamy World
1. LOAD
3. LOAD
4. LOAD
5. MUL
2. SUB
1. LOAD 
3. LOAD 
4. LOAD 
5. MUL
2. SUB 
L1 Cache: 5 cycles 
L1 Cache: 5 cycles 
L1 Cache: 5 cycles 
1 cycle 
2 cycles 
Yippee

## Slide 6: Core, cache, DRAM interaction
Back-end
data
❸
❹
…
L1-I
Core
Front-end
(code)
L2/LLC
L1-D
Unified

## Slide 7: Core, cache, DRAM interaction
Core
$
LOAD X

## Slide 8: Core, cache, DRAM interaction
Core
$
LOAD X
Hit
Data
Few cycles

## Slide 9: On a miss: Critical Word first
Core
$
LOAD X
Data
On a miss, respond with the word/byte requested to the core so that core can continue while fetching the rest of the block
Miss

## Slide 10: On a miss: Early Restart
Core
$
LOAD X
Data
On a miss, fetch the words/bytes in normal order, but as soon as the requested word/byte of the block arrives, send it to the core.
Miss

## Slide 11: Core, cache, DRAM interaction
Core
$
LOAD X
Miss
Data
100s of cycles
I am an out-of-order core
One cache miss and can’t handle anymore misses

## Slide 12: MSHRS (Miss-status holding registers)
Core
$
LOAD X
Miss
Data
X
Non-blocking cache

## Slide 13: MSHRS (Miss-status holding registers)
Core
$
LOAD Y
Miss
Data
X
Y

## Slide 14: MSHRS (Miss-status holding registers)
Core
$
LOAD Z
Miss
Data
X
Y
Z
K-entry MSHR allows K outstanding misses: provides memory-level parallelism

## Slide 15: MSHRS (Miss-status holding registers)
Core
$
LOAD Z
Miss
Data
X
Y
Z
DRAM response time is not constant: can take from 60 cycles to 1000s of cycles (on a multi-core system).

## Slide 16: MSHRS (Miss-status holding registers)
Core
$
LOAD Z
Miss
Data
X
Y
Z
DRAM response time is not constant: can take from 60 cycles to 1000s of cycles (on a multi-core system).

## Slide 17: MSHRS (Miss-status holding registers)
Core
$
LOAD Z
Miss
Data
X
Z
DRAM response time is not constant: can take from 60 cycles to 1000s of cycles (on a multi-core system).

## Slide 18: What about writes (stores)
On a hit: Update the cache block. We need an additional bit in tag-store, named dirty bit along with the valid bit and replacement priority bits.
Write-through cache: On a hit, write into a cache block and also into the next-level in the memory hierarchy
Write-back cache: On a hit, write into a cache block only, and during replacement update the next-level

## Slide 19: What about writes: Writeback cache
Core
$
STORE Z
data
Z

## Slide 20: What about writes: On replacement
Core
$
STORE Z
data
Write-back Buffer

## Slide 21: Write-back cache
Core
$
STORE Z
data
Write-back Buffer
Write-back cache
In general, STOREs are not critical for performance. But why?

## Slide 22: What about a write miss?
Core
$
STORE Z
Miss
Z
LOAD Z
STORE gets converted to a LOAD,
and data is allocated into the cache (write-allocate policy).
Usually write-allocate is used with the write-back caches.

## Slide 23: The Bigger Picture
CPU time = CPU execution cycles + Memory-stall cycles
Clock cycle time may be different
Memory-stall cycles = Read-stalls + Write-stalls
Read/Write stalls =
#Reads/writes X Read/Write miss-rate X Read/write miss-penalty

## Slide 24: Latency Hiding Technique

## Slide 25: Hardware Prefetching
$
Prefetcher
X+2
X+3
Core
X+3
❶
❷
❸
❹
❺
HIT
X+1
X

## Slide 26: 10K Feet View
What?
Latency-hiding technique - Fetches data before the core demands.
Why?
Off-chip DRAM latency has grown up to 400 to 800 cycles.
How?
By observing/predicting the demand access (LOAD/STORE) patterns.

## Slide 27: Prefetch Degree
Prefetch Degree: Number of prefetch requests to issue at a given time.
L2
L3/DRAM
Prefetcher
X
Demand
Access
X+1
X+2
X+1
X+2
X+1
X+3
X+4

## Slide 28: Prefetch Distance
Prefetch Distance: How far ahead of the demand access stream are the prefetch requests issued?
demand access
Prefetch-distance
X
Y
prefetch
Y
= X + 4
Y
= X + 8
Y
= X + 16

## Slide 29: Next-line prefetcher
Next Line: Miss to cache block X , prefetch X+1. Degree=1, Distance=1
Works well for L1 Icache and L1 Dcache.

## Slide 30: What About this?

## Slide 31: Example
for (i = 0; i < N; i=i+16)
sum +=c[i];
c[0]
c[16]
c[32]
c[48]
...
Cache line size of 64B
IPX: LOAD
L1
L0
L2
L3
L4
L5
L6

## Slide 32: IP-stride prefetcher
PC
effective address
instruction tag
previous address
stride
state
-
+
prefetch address

## Slide 33: Metrics of interest
Accuracy
Coverage
Timeliness