## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture-3: Combinational Circuits
https://www.cse.iitb.ac.in/~biswa/courses/CS230/main.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: Contd.
1.
Minterm to Maxterm conversion:
rewrite minterm shorthand using maxterm shorthand
replace minterm indices with the indices not already used
2.
Maxterm to Minterm conversion:
rewrite maxterm shorthand using minterm shorthand
replace maxterm indices with the indices not already used
3.
Expansion of to expansion of :
4.
Minterm expansion of to Maxterm expansion of :
rewrite in Maxterm form, using the same indices as
E.g.,
E.g.,

## Slide 4: K-Maps
Karnaugh Map (K-map) method
  K-map is an alternative method of representing the truth table that helps visualize adjacencies in up to 6 dimensions
  Physical adjacency ↔ Logical adjacency
2-variable K-map
 |  | 00 | 01 | 11 | 10
00 |  | 0000 | 0001 | 0011 | 0010
01 |  | 0100 | 0101 | 0111 | 0110
11 |  | 1100 | 1101 | 1111 | 1110
10 |  | 1000 | 1001 | 1011 | 1010
3-variable K-map
4-variable K-map
 |  | 00 | 01 | 11 | 10
0 |  | 000 | 001 | 011 | 010
1 |  | 100 | 101 | 111 | 110
 |  | 0 | 1
0 |  | 00 | 01
1 |  | 10 | 11

## Slide 5: Coffee points
Why 11 before 10 ?

## Slide 6: Coffee points
Why 11 before 10 ?
Numbering Scheme: 00, 01, 11, 10 is called a
“Gray Code” — only a single bit (variable) changes
from one code word and the next code word

## Slide 7: How? To minimize the Function
Adjacent
000
001
010
011
110
111
100
101
000
001
010
011
110
111
100
101
Adjacent
K-map adjacencies go “around the edges”
Wrap around from first to last column
Wrap around from top row to bottom row
 |  | 00 | 01 | 11 | 10
0 |  | 000 | 001 | 011 | 010
1 |  | 100 | 101 | 111 | 110

## Slide 8: How?
 |  | 00 | 01 | 11 | 10
00 |  | 1 | 0 | 0 | 1
01 |  | 0 | 1 | 0 | 0
11 |  | 1 | 1 | 1 | 1
10 |  | 1 | 1 | 1 | 1
Strategy for “circling” rectangles on Kmap:
As big as possible
Biggest “oops!” that people forget:
Wrap-arounds

## Slide 9: Some more examples

## Slide 10: Some more examples

## Slide 11: Why minimize?
Efficient resource usage
Resource scarcity

## Slide 12: Summary
Very simple guideline:
  Circle all the rectangular blocks of 1’s in the map, using the fewest possible number of circles
    Each circle should be as large as possible
  Read off the implicants that were circled
  Some of them may be “don’t care” (X) Try it yourself

## Slide 13: PAUSE

## Slide 14: Combinational Circuits
Combinational logic is often grouped into larger building blocks to build more complex systems
Hides the unnecessary gate-level details to emphasize the function of the building block
Output is only dependent on the input
We now examine:
  Decoder
  Multiplexer
  Full adder

## Slide 15: Decoder
“Input pattern detector”
n inputs and 2n outputs
Exactly one of the outputs is 1 and all the rest are 0s
The output that is logically 1 is the output corresponding to the input pattern that the logic circuit is expected to detect
Example: 2-to-4 decoder
The complement of a decoder is encoder

## Slide 16: Contd.
n inputs and 2n outputs
Exactly one of the outputs is 1 and all the rest are 0s
The output that is logically 1 is the output corresponding to the input pattern that the logic circuit is expected to detect
Mostly decoders have an enable signal. Output is only generated if the enable is high.

## Slide 18: Multiplexer
Selects one of the N inputs to connect it to the output
  based on the value of a log2N-bit control input called select
Example: 2-to-1 MUX
When S is 0, Y is D0 and when S is 1, Y is D1

## Slide 19: Contd.
Selects one of the N inputs to connect it to the output
  based on the value of a log2N-bit control input called select
Example: 2-to-1 MUX

## Slide 20: From 2 to 4:1 MUX

## Slide 21: Adder

## Slide 22: Half adder

## Slide 23: Full adder

## Slide 24: Implementation

## Slide 25: Ripple Carry Adder

## Slide 26: Comparator (Equality Checker)

## Slide 27: ALU (Arithmetic Logic Unit)