## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 4: Sequential Circuits
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: Sequential Circuit
Combinational circuit output depends only on current input
We want circuits that produce output depending on current and past input values – circuits with memory
How can we design a circuit that stores information?
Sequential Circuit
Combinational
Circuit
inputs
outputs
Storage
Element

## Slide 4: The base for any storage
If Q is zero then Q complement is 1. Note that the circuit has no inputs ☺

## Slide 5: The Clock as some need it
Clock is driven by the slowest combinational circuit/path.
Clock is responsible for triggering a state change

## Slide 6: Clock
Logic beat (like heart beat) oscillates between high and low voltage but at a constant frequency

## Slide 7: Clock and Storage Elements
Storage elements are affected only at the arrival of a clock pulse.
Storage elements are usually called as a latch/flip-flop.
They maintain a binary state until directed by a clock pulse.

## Slide 8: S-R Latch
Cross-coupled NOR/NAND gates
  Data is stored at Q (inverse at Q’)
  S and R are control inputs
  S = Set, Q=1 -> S=1, Q=0; S=0
  R = Reset

## Slide 9: S-R Latch
Three inputs: Set, Reset, and a proxy clock
Circuit works only when the proxy clock is ON S=Set R=Reset

## Slide 10: Contd.

## Slide 11: NAND gates
Cross-coupled NAND gates
  Data is stored at Q (inverse at Q’)
  S and R are control inputs
    In quiescent (idle) state, both S and R are held at 1
    S (set): drive S to 0 (keeping R at 1) to change Q to 1
    R (reset): drive R to 0 (keeping S at 1) to change Q to 0
S and R should never both be 0 at the same time
S
R
Q’
Q
Input |  | Output
R | S | Q
1 | 1 | Qprev
1 | 0 | 1
0 | 1 | 0
0 | 0 | Forbidden

## Slide 12: Why not R=S=0?
1
0
If R=S=0, Q and Q’ will both settle to 1, which breaks our invariant that Q = !Q’
If S and R transition back to 1 at the same time, Q and Q’ begin to oscillate between 1 and 0 because their final values depend on each other (metastability)
  This eventually settles depending on variation in the circuits
S
R
Q’
Q
Input |  | Output
R | S | Q
1 | 1 | Qprev
1 | 0 | 1
0 | 1 | 0
0 | 0 | Forbidden
1
0
0
0
1
1

## Slide 13: Gated D-latch
How do we guarantee correct operation of an S-R Latch?
  Add two more NAND gates!
  Q takes the value of D, when write enable (WE) is set to 1
  S and R can never be 0 at the same time!
S
R
Q’
Q
Write
Enable
D
Input |  | Output
WE | D | Q
0 | 0 | Qprev
0 | 1 | Qprev
1 | 0 | 0
1 | 1 | 1

## Slide 14: Why are latches not preferred? Coffee points++
The inputs should not change while the gate signal is asserted (otherwise there are multiple state changes which can lead to problems in a circuit).

## Slide 15: One Solution
What if we change our states only on clock edge and call me edge-triggered

## Slide 16: Edge Triggering Master-slave D Flip-flop with two latches
Negative edge triggered flipflop
At a given time, only one latch is alive (either master or slave)

## Slide 17: Level/Edge Triggered

## Slide 18: Summary
Gates are building blocks of combinational circuits
Latches are ………………………....... sequential circuits
Latches are built from gates
Flip-flops are built from latches

## Slide 19: Register
D
Q
How can we use D latches to store more data?
Use more D latches!
A single WE signal for all latches for
simultaneous writes
D2
Q2
D1
Q1
D0
Q0
3
3
Write Enable
Here we have a register, or a structure that stores more than one bit and can be read from and written to
This register holds 4 bits, and its data is referenced as Q[3:0]

## Slide 20: Register
How can we use D latches to store more data?
Use more D latches!
A single WE signal for all latches for
simultaneous writes
Here we have a register, or a structure that stores more than one bit and can be read from and written to
This register holds 4 bits, and its data is referenced as Q[3:0]
Register x (Rx)
D3:0
Q3:0
WE
4
4

## Slide 21: Sequential circuit 101 again
Combination of latches/flip-flops and combinational elements (gates).
Flip-flops need a clock

## Slide 22: Coffee Credits
Shreyas: +1

## Slide 23: An Example (Let’s try it)

## Slide 24: State Table
A (t+1) = Ax + Bx, B (t+1) = A`x , y = Ax` + Bx`

## Slide 25: State Diagram x/y where x is input and y is output after the transition

## Slide 26: Try it for a binary counter ☺
Lab-1

## Slide 27: Textbook Reading
H&H, 3.2 and 3.4