## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 5: The D-Day@Digital logic
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: Recap of D Flip-flop

## Slide 4: Recap of D Flip-flop

## Slide 5: Recap of D Flip-flop

## Slide 6: Recap of D Flip-flop

## Slide 7: Recap of D Flip-flop

## Slide 8: Delay to make sure all is well

## Slide 9: More Delay

## Slide 10: All in One

## Slide 11: Revisiting sequential circuit: A complete picture

## Slide 12: State Table
A (t+1) = Ax + Bx, B (t+1) = A`x , y = Ax` + Bx`

## Slide 13: State Diagram x/y where x is input and y is output after the transition

## Slide 14: Try it for a binary counter ☺
Lab-1

## Slide 15: World of State machines (FSMs) Moore and Mealy Machines

## Slide 16: Moore vs Mealy
Moore machine: Output depends on the current state
Mealy machine: Output depends on the current state and inputs

## Slide 17: Odd Parity Checker
0/0
1/1
1/0
0/1
Mealy
Moore
Serial input string
  OUT=1 if odd # of 1s in input
  OUT=0 if even # of 1s in input
Let’s do this for Moore and Mealy

## Slide 18: Try on your own

## Slide 19: State Transitions
Present Input Next Present
State State Output
Even 0 Even 0
Even 1 Odd 0
Odd 0 Odd 1
Odd 1 Even 1
Present Input Next Present
State State Output
Even 0 Even 0
Even 1 Odd 1
Odd 0 Odd 1
Odd 1 Even 0
Moore
Mealy
Output changes only when the state changes
Appears after the state transition takes place
outputs change at clock edge
Even = 0
Odd = 1
Output changes when the state and input changes
Appears before the state transition is completed
React faster to inputs — don't wait for clock

## Slide 20: 01/10 detector: Moore Machine
D/1
E/1
B/0
A/0
C/0
1
0
0
0
0
1
1
1
1
0
reset
current next current reset input state state output
1 – – A 0
0 0 A B 0
0 1 A C 0
0 0 B B 0
0 1 B D 0
0 0 C E 0
0 1 C C 0
0 0 D E 1
0 1 D C 1
0 0 E B 1
0 1 E D 1

## Slide 21: 01/10 detector: Mealy Machine
current next current reset input state state output
B
A
C
0/1
0/0
0/0
1/1
1/0
1/0
reset/0
1 – – A 0
0 0 A B 0
0 1 A C 0
0 0 B B 0
0 1 B C 1
0 0 C B 1
0 1 C C 0

## Slide 22: PAUSE

## Slide 23: Architecture-101

## Slide 24: Next Few Lectures
How can a programmer interact with the processor?
The language of computer: Instructions
Instructions have a vocabulary called instruction set
Driven by instruction set architecture (ISA)
ISA: x86, Arm, RISC-V, MIPS

## Slide 25: Coffee Credits
Anirrudh + 1
Tejas +1