## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 6: Hola Computer Architecture
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Coffee Points Café closed 

## Slide 3: Architecture-101

## Slide 4: Next Few Lectures
How can a programmer interact with the processor?
The language of computer: Instructions
Instructions have a vocabulary called instruction set
Driven by instruction set architecture (ISA)
ISA: x86, Arm, RISC-V, MIPS

## Slide 5: Why MIPS?
Simple yet expressive
Basic principles are similar if not the same. e.g., ARM ISA
Still in use today: embedded devices, routers, modems etc.

## Slide 6: ISA: Abstraction layer
  Interface between hardware and software
  hides complexity from the software through a set of simple instructions

## Slide 7: Abstraction Example: 101
  a = b + c ; // C code
  compiler
  add $1, $2, $3 // assembly language as per the ISA
  assembler
  010101010101010 // machine language, 0s and 1s

## Slide 8: Abstraction Example: 101
Operands can be in registers or in memory
Core
operands
Registers

## Slide 9: A bit detailed
Costly DRAM accesses
Costly: 100 times
Core
South pole 
32-bit Address
Data
GBs DRAM
Registers
Registers are limited

## Slide 10: Instructions
Programmers’ order/command to the processor

## Slide 11: Why Instructions?
Programmer knows what it can/cannot
Processor knows what it should
Power of abstraction:
World with no instructions:
Programmers – communicate a sequence of 0s and 1s

## Slide 12: World with no instructions
000000 00000 00000 00010 00000 100101 000000 00000 00101 01000 00000 101010 000100 01000 00000 00000 00000 000011 000000 00010 00100 00010 00000 100000 001000 00101 00101 11111 11111 111111 000010 00000 10000 00000 00000 000001

## Slide 13: Let’s Open the Processor Core
Register 0
Register 1
Register 2
Register 3

## Slide 14: Let’s Open the Processor Core
Register 0
Register 1
Register 2
Register 3
Arithmetic / Logic Unit

## Slide 15: Let’s put the Memory (not inside the core)
Register 0
Register 1
Register 2
Register 3
Arithmetic / Logic Unit
Bus

## Slide 16: Let’s put the Memory (not inside the core)
Register 0
Register 1
Register 2
Register 3
Arithmetic / Logic Unit
Address Bus
Data Bus

## Slide 17: MIPS Instructions: 101
add $0, $1, $2
add: operation, $0: Destination, $1 & $2: Source(s)
Most of the arithmetic/logical: two sources and one destination

## Slide 18: What to do for “a=b+c-d”?

## Slide 19: What to do for “a=b+c-d”?
add $t0, $s1, $s2 #$t = b+c
sub $s0, $t0, $s3 #$s = $t-d
Temporary register
Try out:
f=(g+h) – (i+j)

## Slide 20: Constants and Immediate
x=x+10
addi $s0, $s0, 10
i: immediate, for constants, constant: 2s complement
No need of a register

## Slide 21: Constants and Immediate
x=x+10
addi $s0, $s0, 10
i: immediate, for constants
constant: 16 bits, 2s complement form
No need of a register
Do we need a subi ? 

## Slide 22: Constants and Immediate
x=x+10
addi $s0, $s0, 10
i: immediate, for constants, constant: 2s complement form
No need of a register
Do we need a subi ? 
NO

## Slide 23: Special treatment for zero
$0 or $zero is a special register that contains ZERO
a=b becomes add $s1 $s2 $zero
Why add if we can move?

## Slide 24: Pseudo Instruction 101
a=b
move $S0, $s1
Not an actual instruction.
It is used for programming convenience

## Slide 25: Logical Operations
Bitwise operations and shifts (Refer Section 2.6 P&H)
sll, srl, and, or, nor, andi, ori etc
No not instruction , well not is nor with one operand=0
32 raw bits instead of a 32-bit number.

## Slide 26: How to store a 32-bit constant into a 32-bit register? Remember 16-bit 
For example, 10101010 10101010 11110000 11110000

## Slide 27: Trivia? How to store a 32-bit constant into a 32-bit register?
For example, 10101010 10101010 11110000 11110000
lui $t0, 0xAAAA #1010101010101010, lower bits all 0s.
ori $t0, $t0, 0xF0F0 #1111000011110000

## Slide 28: Trivia? How to store a 32-bit constant into a 32-bit register?
For example, 10101010 10101010 11110000 11110000
lui $t0, 0xAAAA #1010101010101010, lower bits all 0s.
Basically it will be 0xAAAA0000 (in hexadecimal)
ori $t0, $t0, 0xF0F0 #1111000011110000
it will be 0xAAAAF0F0
lui: upper bits, ori/addi: lower bits

## Slide 29: Coffee Credits
Navya +1
Satyankar +1

## Slide 30: Congrats ISRO, Well Done India
Processor used: Vikram (some avatars of Vikram), 32-bit, 150 instructions
Photo credit: To the owner!