## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 7: MIPS instructions contd.
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: Recap
ISA
Assembly
Machine level
Instructions

## Slide 4: Memory Instructions
Core
lw $t0, 1($a0) # $t0 = Memory[$a0 + 1]
sw $t0, 1($a0) # Memory[$a0 + 1] = $t0
LOAD from memory
STORE into the memory

## Slide 5: Stored Program
Stored Program
&
Von
Neumann

## Slide 6: Memory
4GB of Memory (DRAM)
Say, a word: four bytes

## Slide 7: How to access instructions: Program Counter (PC)
A register that stores the address of the instruction
32-bit processor: addresses are of width 32 bits (devil is in the details  )
So the processor fetches PC, PC+4, PC+8, ….. in a sequential order

## Slide 8: 1946 onwards
Registers,
ALU, PC
Datapath
Memory
(instructions
+data)
Processor
Input
Output
Since 1946 all computers have had 5 components

## Slide 9: Example (Remember PC for the time being)
PCX: lw
PCY: add
PCZ: lui
PCZ=PCY+4 and PCY = PCX+4

## Slide 10: Why Memory? Why Not Registers?
Registers are limited. More #registers, higher access time.
How? we will see sooner than later.
Let’s focus on the data part now. How to access data for our instructions?

## Slide 11: Memory Instructions
Core
lw $t0, 1($a0) # $t0 = Memory[$a0 + 1]
sw $t0, 1($a0) # Memory[$a0 + 1] = $t0
LOAD from memory
STORE into the memory

## Slide 12: LOAD From the Memory (data-transfer insts)
Core
r1
r32
.
.
.
0
1
.
.
.
10
100
.
.
.
Address
Data
lw $t0, 1($a0)
Memory[$a0 + 1]
Load immediate is not a load from memory 

## Slide 13: STORE
Core
r1
r32
.
.
.
0
1
.
.
.
10
100
.
.
.
Address
Data
sw $t0, 1($a0)
Memory[$a0 + 1]

## Slide 14: Both instructions and data from memory
g = h + A [8];
PCX: lw $t0, 8($3) # A[8]
PCY: add $s1, $s2, $t0 # g = h + t0
PCY = PCX+4

## Slide 15: A quick recap
Von Neumann (stored program) concept
As registers are limited, data can be there in the registers or in the memory
Register accesses are through register names/numbers
Memory accesses are through addresses stored in registers

## Slide 16: Let’s move on: Decision Making Instructions
Decisions: if, else ….
Two instructions:
beq (branch equals to) and
bne (branch not equals to)
beq $t0, $t1, L1
bne $t0, $t1, L1

## Slide 17: Branch Instructions: Conditional branches
beq $t0, $t1, L1
goto L1 (statements labeled as L1) if $t0 equals $t1
bne $t0, $t1, L1
goto L1 (statements labeled as L1) if $t0 does not equal to $t1

## Slide 18: The slt instruction (Set on less than)
if (a < b) // beq and bne won’t work here
c=1
else
c=0
slt $t3, $t1, $t2 // t1 and t2 contain a and b
We can slti too; one of the operand will be a constant

## Slide 19: Loops: How to deal with it?
while(CS230[i] == k)
i+=1;
say i and k are in $s3 and $s5, and the
base of CS230 in $s6

## Slide 20: Loops continued
while(CS230[i] == k)
i+=1;
LOAD CS230[i], base address of CS230 is in $s6
We need to go to CS230[i]
Assuming CS230 is an integer array, each index is of 4 bytes. We need to go to CS230 [i*4 bytes]

## Slide 21: Loops contd. ($s3=i, $s5=k, $s6=base address)
sll $t1, $s3, 2 // i*4
add $t1, $t1, $s6 // address of CS230[i]
lw $t0, 0($t1) // t0 = CS230[i]
bne $t0, $s5, Exit // go to Exit if CS230[i] not equals to k
addi $s3, $s3,1 // i=i+1
Exit: // do nothing
while(CS230[i] == k)
i+=1;
Where is the Loop?

## Slide 22: Loops continued
Loop: sll $t1, $s3, 2 // i*4
add $t1, $t1, $s6 // address of CS230[i]
lw $t0, 0($t1) // t0 = CS230[i]
bne $t0, $s5, Exit // go to Exit if CS230[i] not equals to k
addi $s3, $s3,1 // i=i+1
Exit: // do nothing
while(CS230[i] == k)
i+=1;
How to jump to the Loop?

## Slide 23: Loops continued
Loop: sll $t1, $s3, 2 // i*4
add $t1, $t1, $s6 // address of CS230[i]
lw $t0, 0($t1) // t0 = CS230[i]
bne $t0, $s5, Exit // go to Exit if CS230[i] not equals to k
addi $s3, $s3,1 // i=i+1
j Loop // go to loop. j here is jump
Exit: // do nothing
while(CS230[i] == k)
i+=1;

## Slide 24: Textbook Chapter 2 P&H

## Slide 25: Namaste