## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture-8: MIPS Instructions-III
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Sequential execution and jumps
PC, PC+4, PC+8, …………….
PC, PC+4, {if condition here, TRUE} PC+32, ………
j instruction loads an immediate into the PC. It can be either specified as an offset or the label (assembler will convert this label into an offset).

## Slide 3: Functions (Procedures)
int sum(int a, int b)
{
int c=a+b;
return c;
}
void main (void)
{
int i=1;
int j=2;
int k = sum(i,j);
// …..
}

## Slide 4: Simple 
int sum(int a, int b)
{
int c=a+b;
return c;
}
void main (void)
{
int i=1;
int j=2;
int k = sum (i,j);
// …..
}
//jump to function

## Slide 5: Simple 
int sum(int a, int b)
{
int c=a+b;
return c;
}
void main (void)
{
int i=1;
int j=2;
int k = sum(i,j);
// …..
}
j sum
How do you return? 

## Slide 6: Awesome Instructions
jal: Jump and Link and jr $ra
jal L1:
go to L1, the instruction that has to be executed next is in L1.
and
save the address of the next instruction in $ra. ra is an awesome register that stores the return address.

## Slide 7: Awesome Instructions
jal: Jump and Link and jr $ra
jal L1:
go to L1, the instruction that has to be executed next is in L1.
and
save the address of the next instruction in $ra. ra is an awesome register that stores the return address (ra).
Go to instruction whose address is stored in ra (PC+4)

## Slide 8: Let’s Have a Complete Picture
PC+4 addi $R1, $R0, 2 // R0 = 0, R1=2
PC+8 jal sum // R31 (ra) = PC+12
PC+12 add $R0, $R3, $R3
sum:
PC+100 addi $R2, $R1, 4
PC+104 jr

## Slide 9: Let’s Have a Complete Picture
PC+4 addi $R1, $R0, 2 // R0 = 0, R1=2
PC+8 jal sum // R31 = PC+12 (ra)
PC+12 add $R0, $R3, $R3
sum:
PC+100 addi $R2, $R1, 4 // R2 =6
PC+104 jr $R31

## Slide 10: Let’s Have a Complete Picture
PC+4 addi $R1, $R0, 2 // R0 = R3 = 0, R1=2
PC+8 jal sum // R31 = PC+12 (ra)
PC+12 add $R0, $R3, $R3 // R0 = 0
sum:
PC+100 addi $R2, $R1, 4 // R2 =6
PC+104 jr $R31

## Slide 11: Let’s Have a Complete Picture
PC+4 addi $R1, $R0, 2 // R0 = R3 = 0, R1=2
PC+8 jal sum // R31 = PC+12 (ra)
PC+12 add $R0, $R2, $R2 // R0 = 12
sum:
PC+100 addi $R2, $R1, 4 // R2 =6
PC+104 jr $R31

## Slide 12: JAL: Jump and Link, What’s wrong?
PC+4 addi $R1, $R0, 2
PC+8 jal sum // R31 = PC+12 (ra)
PC+12 add $R0, $R2, $R2

## Slide 13: Well
As per MIPS specification, Check P&H MIPS sheet 
PC: jal label ra = PC + 8
PC+4:
PC+8:

## Slide 14: PC+4 or PC+8? Why this
PC+4 at the moment
PC+8 after a month or so 

## Slide 15: PAUSE: Quick recap
Usage of j, jr, jal, and $ra

## Slide 16: MIPS provides
Upto four arguments can be passed from the caller to the callee while using jal. It uses registers $a0 to $a3
A callee can return upto two values to the caller. It uses registers $v0 and $v1

## Slide 17: What if?
main(){
a = a + f1(a);
} f1:
f1(a) { f2’s argument in $a0 to $a3
a = a - f2(a); return a;} jal f2
f2(a) {
a = a + f3(a); return a;}
f3(a) {
a = a + 1; return a;}

## Slide 18: What if?
f1:
f2’s argument in $a0 to $a3
jal f2
…
f2:
f3’s argument in $a0 to $a3
jal f3
…

## Slide 19: What is the big deal?
f1:
f2’s argument in $a0 to $a3
jal f2
…
f2:
f3’s argument in $a0 to $a3
jal f3
...

## Slide 20: What is the big deal? Oh no!
f1:
PC: f2’s argument in $a0 to $a3
PC+4: jal f2 // $ra = PC+8
…
f2:
PC+100: f3’s argument in $a0 to $a3
PC+104: jal f3 // $ra = PC+108
f3: …
... jr $ra

## Slide 21: What is the big deal? Oh no!
f1:
PC: f2’s argument in $a0 to $a3
PC+4: jal f2 // $ra = PC+8
…
f2:
PC+100: f3’s argument in $a0 to $a3
PC+104: jal f3 // $ra = PC+108
jr $ra  Oh no!! f3: …
... jr $ra

## Slide 22: Saving and Restoring Registers (limited)
caller registers
callee registers
Why?
Callee does not know, registers used by callers, can be many callers too
Caller does not know the callee’s plan 

## Slide 23: Do not forget 32 MIPS registers only Register spilling 

## Slide 24: Quick recap
Register spilling, 32 MIPS registers, nested functions,
oh no!
Spilled registers: Where else can we store?

## Slide 25: The loaded program
System program that loads the executable into the memory.
Every executable has a text, heap/stack data segments

## Slide 26: MIPS way of handling it: The Stack (part of DRAM, for each function call)
Stores caller data
$sp (stack pointer) points to the address where stack ends
One per function, private memory area, else the same problem 
Stack grows down

## Slide 28: MIPS way of handling it: Before function call
sp
Caller

## Slide 29: MIPS way of handling it: Function call is ON
sp
Caller R1
Callee R2
Callee R4
Saved

## Slide 30: MIPS way of handling it: After the function call
sp
Caller R1

## Slide 31: How to save and restore?
Save:
addi $sp, $sp, -4
sw R4, ($sp)
Restore:
lw R4, ($sp)
addi $sp, $sp, 4
32 bit registers, 4 bytes, one word, remember
sp
Callee R4
Saved
sp
Restored
Caller R1
Caller R1

## Slide 32: Nested Functions (Remember main() is a function too  )
CS230 // jal cs230
{
CS330 // jal cs330
{
CS430 // jal cs430
{
} //jr
} //jr
} // jr

## Slide 33: The final one: Frame pointer
Stack also stores local variables and data structures (local arrays and structures) for a function along with the return address(es).
Frame pointer will get incremented and decremented based on the local arguments used.

## Slide 34: The final one: Frame pointer
Frame pointer: Points to local variables and saved registers. Points to the highest address in the procedure frame. Stays there throughout the procedure. Stack pointer, moves around.
sp
regs.
fp
returns
sp
fp
sp
fp
Awesomeness: You can access any using fp/sp and an offset
local

## Slide 35: Try This Out! Discuss on Piazza
Page no A-27 to A-29 P&H
Recursive function fact(n)
Look for sp, fp, ra, jal, and jr

## Slide 36: For the Curious Ones (Beyond CS230)
Stack buffer overflow - 101: https://en.wikipedia.org/wiki/Stack_buffer_overflow

## Slide 37: Coffee credits
Ankeet +5

## Slide 38: ਸਤਿ ਸ੍ਰੀ ਅਕਾਲ