## Slide 1: CS230: Digital Logic Design and Computer Architecture
Lecture 9: Instruction Decoding and addressing modes
https://www.cse.iitb.ac.in/~biswa/courses/CS230/autumn23/main.html

## Slide 2: Why instruction decoding?
Core
Based on PC
LOAD inst. from memory

## Slide 3: Instruction received then what?
Core
Remember instructions are of 32-bit size (in MIPS),
so PC+4
How will the processor know what to infer from these 32 bits?
Simple: Have a decoder 

## Slide 4: Instruction Decoding
op
rs
rt
Immediate
6 bits, maximum
64 operations
add
sub
mul
lw
bne …….
5 bits, 32 registers
(R0 to R31)
16 bit constant
0
31
5 bits, 32 registers (R0 to R31)
21
26
16

## Slide 5: Let’s have a look
rs
rt
funct
op
rd
shamt
0
31
21
26
16
6
11
rs
rt
Immediate
op
0
31
21
26
16
Target jump address
op
0
31
26
R-type
I-type
J-type

## Slide 6: 10K Feet View of MIPS encoding
rs
rt
funct
op
rd
shamt
Why this field?
Wastage of space 

## Slide 7: Good design demands good compromises
Instruction | Format | op | rs | rt | rd | shamt | funct | address
add | R | 0 | reg | reg | reg | 0 | 32 | n.a.
sub | R | 0 | reg | reg | reg | 0 | 34 | n.a.
addi | I | 8 | reg | reg | n.a. | n.a. | n.a. | constant
lw | I | 35 | reg | reg | n.a. | n.a. | n.a. | address
sw | I | 43 | reg | reg | n.a. | n.a. | n.a. | address
tells how to treat the last set of fields:
three fields or one field, still why funct 

## Slide 8: Why not?
rs
rt
op+funct
rd
shamt
0
31
20
15
5
10
rs
rt
Immediate
op
0
31
21
26
16
Target jump address
op
0
31
26
R-type
I-type
J-type

## Slide 9: What is a good compromise?
Fixed length instructions  32-bit irrespective of ops
Fields are at the same or almost same location
All formats look similar

## Slide 10: Addressing Modes (How and where to find the data)

## Slide 11: Five Common Addressing Modes
Immediate
addi $t0, $t1, 5
op
rs
rt
Immediate

## Slide 12: Five Common Addressing Modes
Register
add $t0, $t1, $t2
rs
rt
funct
op
rd
Register

## Slide 13: Five Common Addressing Modes
Base (Arrays, structures, pointers)
lw $t1, 4($s2)
lw $t1, ($s2) #indirect addressing
rs
rt
Address
op
Register
Memory
±

## Slide 14: Five Common Addressing Modes
PC-relative (e.g., conditional branches, need an offset)
beqz $t0, goEnd
rs
rt
Address (offset)
op
PC
Memory
±

## Slide 15: Five Common Addressing Modes
Pseudodirect
Address
op
PC
Memory
concat
jal
Takes upper four bits of PC and concatenate 26 bits from address field and then
add two zeros at the lsb. PS: It is for unconditional jumps.

## Slide 16: Endianness (Byte ordering within a word)
Big Endian: address of most significant byte = word address (xx00 = Big end of word), MIPS
Little Endian: address of least significant byte = word address (xx00 = Little end of word), x86
Think about an egg 
msb
lsb
3 2 1 0
little endian byte 0
0 1 2 3
big endian byte 0

## Slide 17: Just for an example, do not take it for granted …
unsigned int i = 1;
char *c = (char*)&i; // reading the LSB
Printf (“%d”, *c);
unsigned int i = 12345678;
char *c = (char*)&i;
Printf (“%d”, *c);

## Slide 18: Example
unsigned int i = 1;
char *c = (char*)&i; // reading the LSB
Printf (“%d”, *c);
Little endian: 1
Big endian: 0
unsigned int i = 12345678;
char *c = (char*)&i;
Printf (“%d”, *c);
Little endian: 78
Big endian: 12

## Slide 19: Coffee credits
Hari: +1

## Slide 20: নমস্কার